## Slide 1: eBGP Introduction
4 March 2016
José Bernardo Lozano
Technical Manager, Cisco Networking Academy

## Slide 2: BGP Overview
BGP Objectives:
  Exchange Public Networks between different Autonomous Systems (ASs)
  Manipulate Incoming and Outgoing paths for Network Updates
  Rich Manipulation and Filtering Tools.
BGP Basic Configuration:
  Session Establishment between Neighbors
  Internal BGP (iBGP): Neighbors in the same AS. More complex than External BGP -Out of scope-
  External BGP (eBGP): Neighbors in different AS.
  Network Updates between Neighbors
  Advertise the networks we want reachability
  A router can advertise any route in its routing table

## Slide 3: eBGP Basic Configuration Example
Scenario:
  Consider 10.0.0.0 address as Public
  Consider 172.16.0.0 address as Private
Objective:
  R1 will advertise 10.1.1.0/24 and 10.1.2.0 / 24 to R4
  R4 will advertise 10.2.1.0 /24 to R1

## Slide 4: eBGP Basic Configuration Steps
Configure and Verify Neighbors
Advertise Networks
  Verify BGP only advertises networks available in Routing Table, no matter if they are directly connected.

## Slide 5: eBGP Basic Configuration Example
Neighbors configuration and verification:
R1(config)# router bgp 65501
neighbor 10.1.4.4 remote-as 65502
R4(config)# router bgp 65502
neighbor 10.1.4.1 remote-as 65501

## Slide 6: eBGP Basic Configuration Example
Neighbors configuration and verification:
R1#show ip bgp neighbors
BGP neighbor is 10.1.4.4, remote AS 65502, external link
BGP version 4, remote router ID 10.2.1.4
BGP state = Established, up for 00:07:17
… (output omitted)
R4#show ip bgp neighbors
BGP neighbor is 10.1.4.1, remote AS 65501, external link
BGP version 4, remote router ID 10.1.1.1
BGP state = Established, up for 00:08:04
… (output omitted)

## Slide 7: eBGP Basic Configuration Example
Networks Advertisements and Verification:
  R1 configured to advertise both networks, only advertises directly connected. R4 only learns directly connected to R1.
  Reason: 10.1.2.0/24 is not on R1 Routing Table.
R1(config)# router bgp 65501
neighbor 10.1.4.4 remote-as 65502
network 10.1.1.0 mask 255.255.255.0
network 10.1.2.0 mask 255.255.255.0
R4#show ip bgp
BGP table version is 6, local router ID is 10.2.1.4
(… output omitted)
Origin codes: i - IGP, e - EGP, ? - incomplete
RPKI validation codes: V valid, I invalid, N Not found
Network Next Hop Metric LocPrf Weight Path
*> 10.1.1.0/24 10.1.4.1 0 0 65501 i

## Slide 8: eBGP Basic Configuration Example
Networks Advertisements and Verification:
  Eigrp configuration on R1 to make 10.1.2.0 available on R1 Routing Table:
R1(config)# router bgp 65501
neighbor 10.1.4.4 remote-as 65502
network 10.1.1.0 mask 255.255.255.0
network 10.1.2.0 mask 255.255.255.0
!
router eigrp 1
network 10.0.0.0
network 172.16.0.0
passive-interface Serial1/0
!
R1#sh ip route eigrp
(… output omitted)
10.0.0.0/8 is variably subnetted, 5 subnets, 2 masks
D 10.1.2.0/24 [90/156160] via 172.16.1.2, 00:11:22, FastEthernet0/0

## Slide 9: eBGP Basic Configuration Example
Networks Advertisements and Verification:
  R4 shows both networks from R1
R4#show ip bgp
BGP table version is 7, local router ID is 10.2.1.4
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,
r RIB-failure, S Stale, m multipath, b backup-path, f RT-Filter,
x best-external, a additional-path, c RIB-compressed,
Origin codes: i - IGP, e - EGP, ? - incomplete
RPKI validation codes: V valid, I invalid, N Not found
Network Next Hop Metric LocPrf Weight Path
*> 10.1.1.0/24 10.1.4.1 0 0 65501 i
*> 10.1.2.0/24 10.1.4.1 156160 0 65501 i

## Slide 10: eBGP Full Configuration
Full R1 and R4 Configuration
R1(config)# router bgp 65501
neighbor 10.1.4.4 remote-as 65502
network 10.1.1.0 mask 255.255.255.0
network 10.1.2.0 mask 255.255.255.0
!
router eigrp 1
network 10.0.0.0
network 172.16.0.0
passive-interface Serial1/0
R4(config)# router bgp 65502
neighbor 10.1.4.1 remote-as 65501
network 10.2.1.0 mask 255.255.255.0

## Slide 11: eBGP Verification
R1# show ip bgp
BGP table version is 8, local router ID is 10.1.1.1
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,
r RIB-failure, S Stale, m multipath, b backup-path, f RT-Filter,
x best-external, a additional-path, c RIB-compressed,
Origin codes: i - IGP, e - EGP, ? - incomplete
RPKI validation codes: V valid, I invalid, N Not found
Network Next Hop Metric LocPrf Weight Path
*> 10.1.1.0/24 0.0.0.0 0 32768 i
*> 10.1.2.0/24 172.16.1.2 156160 32768 i
*> 10.2.1.0/24 10.1.4.4 0 0 65502 i
Some codes:
  * Available Path, not selected by BGP Algorithm
  *> Path Selected by BGP Algorithm.
  Will be registered in IP Routing table.
  Next Hop = 0.0.0.0 for Directly Connected Networks
  Path = AS PATH

## Slide 12: eBGP Verification
R4# show ip bgp
BGP table version is 8, local router ID is 10.2.1.4
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,
r RIB-failure, S Stale, m multipath, b backup-path, f RT-Filter,
x best-external, a additional-path, c RIB-compressed,
Origin codes: i - IGP, e - EGP, ? - incomplete
RPKI validation codes: V valid, I invalid, N Not found
Network Next Hop Metric LocPrf Weight Path
*> 10.1.1.0/24 10.1.4.1 0 0 65501 i
*> 10.1.2.0/24 10.1.4.1 156160 0 65501 i
*> 10.2.1.0/24 0.0.0.0 0 32768 i
Some codes:
  * Available Path, not selected by BGP Algorithm
  *> Path Selected by BGP Algorithm
  Will be registered in IP Routing table.
  Next Hop = 0.0.0.0 for Directly Connected Networks
  Path = AS PATH

## Slide 13: Reachability to eBGP Advertised Networks
R1(config)# router eigrp 1
network 10.0.0.0
network 172.16.0.0
redistribute bgp 65501 metric 64 100 255 1 1500
passive-interface Serial1/0
R2#sh ip route eigrp
…
10.0.0.0/8 is variably subnetted, 5 subnets, 2 masks
D 10.1.1.0/24 [90/156160] via 172.16.1.1, 01:42:43, FastEthernet0/0
D 10.1.4.0/24 [90/2172416] via 172.16.1.1, 01:42:43, FastEthernet0/0
D EX 10.2.1.0/24 [170/40028160] via 172.16.1.1, 00:04:59, FastEthernet0/0
R4# ping 10.1.2.2 source 10.2.1.4
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.1.2.2, timeout is 2 seconds:
Packet sent with a source address of 10.2.1.4
!!!!!
Complex topic, not a simple solution
  Example: R1 Eigrp, does not learn R1 BGP network from R4. Eigrp R1 does not advertise 10.2.1.0 /24 to R2
  Solution: Redistribute BGP into EIGRP. Not recommended without filtering.